GPU & CPU implementation of Young - Van Vliet's Recursive Gaussian Smoothing Filter
Release 0.01

...1, ...2, ...3

June 6, 2013
1Asclepios Research Group, INRIA Sophia Antipolis
2VISAGES Research Group, INRIA Rennes
3Mauna Kea Technologies, Paris
Abstract

This document describes an implementation for GPU and CPU of Young andVan Vliet's recursive gaussian smoothing as an external module for the Insight Toolkit ITK www.itk.org. The code of the algorithm is written following the ITK CodingStyle as described in the directory Insight/Documentation/Style.pdf
This paper is accompanied with the source code, input data, parameters and output data
used for validating the algorithm described in its original papers.

Contents

# Introduction
ITK provides a recursive Gaussian smoothing filter based on the work of Deriche [1]. Young and Van Vliet proposed a different recursive implementation, a computationally efficient forwards and backwards IIR filter [2], [3]. In their implementation, the backwards IIR filter ran on the forward filter output, as opposed to Deriche's recursive filter. The original Young and Van Vliet recursive IIR filter also addressed a ringing artefact found in the Deriche recursive filter [2]. However, it presented certain distortions at the right boundary that Triggs and Sdika addressed in [4] with a different initialization of the backward running coefficients. In turn, a slight modification -acknowledged in Triggs' paper- was introduced by J.-M. Geusebroek [5].
ITK provides GPU support, based on OpenCL, as of v4.0. In this work we present an implementation for both GPU and CPU of the Young and Van Vliet recursive filter with the mentioned improvements. The implementations are provided as an external ITK module and can be used as any other ImageToImageFilter of the framework, independently.
The motivation behind this is offering both alternatives that will suit different hardware configurations (mainly the individual performance capabilities of the CPU and the GPU separately).
# Hardware and Software Requirements
To use only the CPU implementation, you need to have the following software installed:
- Insight Toolkit 4.0 or better.
- CMake 2.6 or better
To use the GPU implementation, the following software is required:
- Insight Toolkit 4.3 or better.
- OpenCL SDK of your GPUs vendor. (Nvidia with support for double precision operations is preferred, although the code has been run successfully on single precision and on an ATI HD Radeon 6970)
- CMake 2.6 or better.
Any OpenCL-compliant GPU should be able to run the code. NVidia with support for double precision operations is preferred, although the code has been run successfully on single precision and on an ATI HD Radeon 6970).
# Users Guide
Both the CPU and GPU smoothing filters can be used as any other itk::ImageToImageFilter, from which they derive. As with other GPU filters in ITK, our GPU filters use images of type itk::GPUImage as input. They are initialised as any other itk::Image. A good precaution is to know the GPU you intend to use: whether it supports double precision or not, in order to avoid creating a double precision GPUImage that will not be handled correctly by the hardware and will return an OpenCL error message.
One peculiarity of GPU filters in the ITK framework to bear in mind is the fact that CPU and GPU memory is synchronised explicitly by the calling
GPUFilter->GetOutput()->UpdateBuffers();
It is at this point where the GPU will send the calculated data back to the CPU.
For further details on the integration of both the CPU and the GPU filters, please refer to the test code included with the module.
During configuration with CMake, there are some options that can be selected:
NVIDIA_GPU: setting this to true activates several optimisations specific to Nvidia GPUs.
GPU_HANDLES_DOUBLE: setting this to true enables double-precision operations. The user must know that the GPU to be used is capable of these and accepts the OpenCL directive cl_khr_fp64.
Double-precision support is also checked at configuration time (via Cmake's TRY_RUN macro): a simple piece of code probes available platforms and devices and, if any devices is found not to support double-precision, this option will be disabled.
# CPU implementation of the Recursive Gaussian Filter
The CPU implementation is based on ITK's support for multithreading and the possibility of separating the passes on each dimension. For each thread, the causal and anticausal filters are applied successively on each line of the image.
It must be noted that the method
RecursiveLineYvvGaussianImageFilter<TInputImage,TOutputImage>
::EnlargeOutputRequestedRegion(DataObject *output)
has been overloaded to assure that the full region was used to calculate the filtered result, regardless of the output region requested.
Both implementations presented take into account both improvements mentioned in the Introduction: the different intialization of the backward running coefficients proposed by Triggs and Sdika in [4] and the slight modifications -acknowledged in Triggs' paper- introduced by J.-M. Geusebroek [5].
# GPU Programming with OpenCL
It has been discussed [6] that recursive algorithms perform poorly on GPUs, given that the margin for parallelization is rather small. This is indeed a challenge, but given the speed at which GPU architectures are developing, it is increasingly common to find systems in which even a recursive Gaussian will perform better on an off-the-shelf dedicated GPU than on a middle-of-the-road CPU.
Several strategies have been followed to improve the performance of the GPU implementation.
Parallelisation by line
The GPU implementation follows on the same multithreaded structure and adapts it to the GPUs workitems. Given that, in the Young-Van-Vliet´s recursive Gaussian filter, the anticausal filter takes the output of the causal filter as input, one workitem will apply both filters sequentially on one line of the image in a given dimension. For 2D images, a 1D GPU kernel will be launched; for 3D images, 2D kernels will be used, in order to maximise parallelism.

Figure 1 The figure shows the notion of a 2D kernel (a 2D grid of workitems) that will process the 3D volume in each dimension sequentially.
This is implemented in the GPU kernel method
__kernel void partialFilter(
__global const INPIXELTYPE* data,
__global OUTPIXELTYPE* outs,
__local REALTYPE* Bvalues,
__local REALTYPE* MMatrix,
unsigned int start,
unsigned int step,
unsigned int length )
This method is called in exactly the same way regardless of the dimension (1D, 2D, 3D) of the data to be smoothed.
As an example, in a 3D volume, the line smoothing for dimension Y will be launched as:
        if(giy < DEPTH && gix < WIDTH) {
partialFilter(data, outs, Bvalues, MMatrix,
giy*WIDTH*HEIGHT + gix, WIDTH, HEIGHT);
}
In this case, gix and giy identify each workitem uniquely in the 2D grid. Each workitem will know its starting point in the volume of data, depending on this unique id, the length of the vector it needs to process (first with the causal filter, then with the anticausal) and the step it needs to apply to read the next pixel to process.
Use of shared and local memory
Another standard strategy to reduce computation time is the use of shared and local memory where possible. To avoid reading from global memory in each calculation, the output of the causal filter is stored in a local memory (i.e. registry-like) array, only accessible by the workitem, and from which the anticausal filter will read. This way, the input data stored in global memory will only be accessed by the causal pass and the results will then be stored in a local vector.
For reference, preliminary tests indicated that, for a 512x512 double image processed on an nVidia GTX 650, the reduction obtained from not writing the result of the causal pass to global image was of 5.51ms to 4.38ms.
Also, both matrices sent to the GPU are stored in shared memory (visible by all workitems in a workgroup) to avoid reading from global memory for every calculation. Several workitems cooperate to load the values of these matrices simultaneously.
Fusion of kernels
To avoid unnecessary CPU-GPU synchronization, it is necessary to apply what Nehab et al. called kernel fusion [7]. On the one hand, as mentioned above, the causal and anti-causal passes (which could have been separated into two independent kernels) have been fused. This is particularly necessary for the Young and Van Vliet IIR filter since the boundary conditions for the transition to the anticausal filter are initialised using the output values of the causal filter.
On the other hand, each dimension is processed sequentially using as input the output image of the previously filtered dimension, without copying the data on the GPU back to the CPU. It is crucial to avoid a CPU-GPU synchronization at this point and allow each call of the kernel to access the image stored on GPU memory.
Workgroup sizes
The number of workitems to a workgroup is directly related to the number of lines to be processed in a given dimension. It is extremely important to minimise both control divergence and the number of workitems idle.
In the implementation we propose, this is crucial for 3D volumes of different sizes in each dimension. To better understand this, let us imagine a 1024x512x16 sequence. Each dimension will be smoothed separately.
- When filtered in the X dimension the kernel will see the volume as a stack of 1024 images of size 512x16 images. This means that our 2D workitem grid should be 512x16 and each workitem will process a vector of length 1024.
- When filtered in the Y dimension the kernel will see it as a stack of 512 images of size 1024x16 images. This means that our 2D workitem grid should be 1024x16 and each workitem will process a vector of length 512.
- Lastly, it follows that in the Z dimension we will need a 1024x512 2D grid of workitems, each of which will process a data vector of length = 16.
If each kernel call is made with the same grid size (i.e. the same global workgroup sizes in both dimensions), and given that only workitems within the boundaries of the volume will have data to process, performance will suffer due to idle workitems and control divergence.
To prevent this, it is necessary to set the global workgroup sizes to sizes close to that of the volume.
For reference, failing to do this in a 3D volume of 1024x1024x16 caused an increase of time of 38.63ms to 272.43ms.
Unrolled loops
Loops inside a kernel must be avoided wherever possible. A workaround is to unroll the loops explicitly or using compiler directives such as #pragma unroll [factor]. Certain compilers (e.g. nVidia) unroll loops by default whenever they are controlled by a constant value known at compilation time. However, this is not a requirement in OpenCL specifications (as of 1.1 and 1.2) and failing to unroll the loops either explicitly or via a pragma directive can potentially decrease performance.
# Results
We present here a subgroup of our results, for different sizes of 2D and 3D images, and sigma = 12. These results were obtained from a machine with the following configuration:
- Intel i7-3770S (8 threads, 4 cores at 3.10GHz),
- 16GB of RAM
- nVidia GeForce GTX650 with 1GB DDR5 RAM (384 cores at 1GHz)
- nVidia drivers 304.84 on Ubuntu.
Times
The results show the performance of two CPU implementations (the Young-Van Vliet and the Deriche) and two variations of the GPU Young-Van Vliet implementation (including all data transfers between CPU and GPU and without these data transfer times). The aim of these two GPU times is to show the overhead introduced by data synchronization.
For 2D images (Figures 2 and 3), the bigger the size, the better the performance factor on GPU. Including GPU-CPU synchronization overheads, we have obtained a x2 acceleration factor. Without including these overheads (e.g. considering the smoothing as part of a bigger pipeline), the acceleration factor is x24.
For 3D images (Figures 4 and 5), the maximum acceleration factor including data transfers was x2.8, whereas without this overhead the acceleration obtained was 31.6.

Figure 2 Results for 2D images, processing with double precision (time in log scale).

Figure 3 Results for 2D images, processing with single precision (time in log scale).

Figure 4 Results for 3D images, processing with double precision (time in log scale).

Figure 5 Results for 3D images, processing with single precision, (time in log scale).

It is also interesting to see how this GPU implementation of a recursive Gaussian smoothing performs compared to the discrete Gaussian smoothing.

Figure 6 Brief comparison between CPU and GPU implementations of Discrete Gaussian smoothing and Recursive Gaussian smoothing (3D).

Figure 7 Brief comparison between CPU and GPU implementations of Discrete Gaussian smoothing and Recursive Gaussian smoothing (2D).
Image quality
The difference between CPU and GPU implementations has been measured on the following image (Figure 8). Figures 9 and 10 show the results of smoothing it with sigma = 12 (or variance = 144 in the case of ITK's discrete gaussian smoothing filter), while Figures 11 and 12 show (in logarithmic scale) the root mean square of the difference, pixel by pixel, between the images as smoothed by the CPU and the GPU implementation. The original image, scaled at different sizes, is a JPEG with integer values between 0 and 255.
Figure 8 Original image. Value range: [0, 255].

Figure 9 Smoothed image with [left] CPU and [right] GPU implementations, sigma=12. (Operations in single precision, float.)

Figure 10 Smoothed image with [left] ITK's (CPU) Deriche recursive gaussian smoothing filter and [right] ITK's CPU discrete gaussian smoothing filter, sigma=12 for the recursive filter, variance= 144 for the discrete filter. (Operations in single precision, float.)
Figure 11 RMS of the difference between the CPU-smoothed image and the GPU-smoothed image, log scale. (Operations in single precision.)

Figure 12 RMS of the difference between the CPU-smoothed image and the GPU-smoothed image, log scale. (Operations in double precision.)
# Discussion
This GPU implementation has a strong limitation in the amount of shared memory available, since all intermediate values are stored per workitem on its local memory. Until recently, as shown in studies such as [6], this was a very important reason why recursive algorithms performed poorly on GPUs [7], as opposed to convolution-based algorithms. More recent architectures (e.g. nVidia's Fermi) provide increased shared memory.
An important aspect of GPU programming is the overhead introduced in data synchronization between CPU and GPU. For each smoothing process, the whole input image -as well as any other data required for the operations- is copied to the GPU and the whole output image is copied back to the CPU. The time required without including data synchronization is shown under “GPU YVV no sync”. GPU implementations become particularly efficient when several processes can be applied without requiring data to be copied back and manipulated in the CPU (e.g. a pipeline chaining several filters).
This can be observed in the times that include these data transfers. The maximum acceleration that was obtained with the GPU implementation was a x33 factor between the CPU and the GPU implementation of the Young-Van-Vliet algorithm on 3D images, without considering the overheads. The acceleration obtained when including the synchronization overheads was x3.5.
For 2D images, this improvement was more discrete, with a maximum acceleration of x24 without overheads and x2.2 with the synchronization overheads.
To put these results in context, it is also interesting to compare them with the Discrete Gaussian (CPU and GPU) implementations already available on ITK (Figures 6 and 7). Both results show that a GPU implementation of the recursive Gaussian filter is a valid alternative to the GPU discrete Gaussian filter in terms of time, even for smaller 2D images. The choice of one over the other depends above all on the power of the CPU and the GPU available, the memory available on the GPU (which, as already mentioned, may hinder recursive algorithms) and the dimensionality of the images.
Thus, it can be argued that with recent GPU architectures, different algorithms need to be benchmarked against the specific needs: 3D images vs. 2D images, CPU and GPU configurations, or the necessary kernel sizes to evaluate the cost of a convolution-based approach.
A possible alternative to this GPU implementation of a recursive gaussian could be to adapt the Deriche version instead, given that the causal and anti-causal passes can be applied simultaneously (thus giving additional margin for parallelisation).
Finally, the differences between CPU and GPU results for floating-point operations must be addressed. Floating-point precision in GPUs has been discussed extensively and Whitehead and Fit-Florea address it regarding Nvidia GPUs specifically (such as the ones used to obtain the results shown here) in [8].
Given how GPUs capable of double-precision operations are widely available, it is advised to use double-precision operations for the algorithm presented here (option “GPU_HANDLES_DOUBLE” during configuration, as mentioned in Users Guide).
# Conclusions
An implementation of the Young-Van-Vliet recursive Gaussian filter has been presented for CPU and GPU. It has been discussed that the GPU implementation is a valid alternative to GPU-based discrete Gaussian smoothing and how the choice of one or other algorithm and implementation depends strongly on the hardware configuration (powerful CPU, GPU or both) available to the user.

Reference